## Slide 1
Health and Medical Sciences · Experimental project
Night Signal.
How accurately can a low-cost wearable measure blood oxygen?
Gabriel Mamane · Grade ___
Educational prototype. It measures SpO₂ and heart rate; it does not diagnose sleep apnea.
Notes: [0:15] Good morning. My name is Gabriel Mamane. My project, Night Signal, asks how accurately a low-cost wearable can measure blood oxygen and heart rate, and whether software can flag drops in oxygen. It is not a test for sleep apnea.

## Slide 2
Purpose and hypothesis
Is a low-cost oxygen wearable accurate?
Question
How closely do SpO₂ and heart-rate readings from a MAX30102 + ESP32 wearable agree with a Health Canada-authorized fingertip pulse oximeter, and can software reliably flag oxygen desaturation events (≥ 3 points for ≥ 10 s)?
Hypothesis
If the wearable is worn correctly and only good-quality readings are used, its SpO₂ will agree with the reference within about ±3 percentage points (95% limits of agreement), because both measure red/infrared light absorption.
Independent variables
Measuring device (wearable vs reference); test condition (seated rest; optional breath-holds only if approved)
Dependent variables
Device − reference difference (bias, 95% limits, mean error); desaturation events flagged; % valid signal
Controls
Same participant, finger, cuff tightness, room and lighting; paired readings every 2 min; same settings
Night Signal
2
Notes: [0:45] My question is how closely my wearable's oxygen and heart-rate readings agree with a Health Canada-authorized fingertip oximeter, and whether software can reliably flag oxygen desaturation events. My hypothesis is that, when it is worn properly and only good-quality readings are used, it will agree within about three percentage points, because both devices measure how blood absorbs red and infrared light. What I change is the measuring device and the test condition; what I measure is the difference between the two devices, the events flagged, and how much of the signal is valid.

## Slide 3
Scientific background
An oxygen dip is a clue, not a diagnosis.
Pulse oximetry: red (660 nm) and infrared (880 nm) light shine through the fingertip. Oxygen-rich and oxygen-poor blood absorb them differently, giving SpO₂.
A desaturation is a short drop in SpO₂. Sleep studies count drops of 3% or more, alongside other signals.
Sleep apnea is diagnosed with a sleep study that also measures airflow, breathing effort and sleep. Oxygen alone cannot do this.
Not every oxygen drop is an apnea (movement, poor contact, other causes), and not every apnea causes a large drop.
936 million
adults worldwide are estimated to have obstructive sleep apnea, and most are undiagnosed (Benjafield et al., 2019).
SpO₂
can show oxygen dips
Heart rate
can show pulse changes
Not measured
airflow · breathing effort · sleep stage
Night Signal
3
Notes: [0:50] A pulse oximeter shines red and infrared light through the fingertip; oxygen-rich and oxygen-poor blood absorb them differently, which gives the oxygen saturation, SpO2. A desaturation is a short drop in SpO2, and sleep studies count drops of three percent or more, but only together with other signals. Sleep apnea is diagnosed with a sleep study that measures airflow, breathing effort and sleep itself. My device measures only oxygen and heart rate, so it cannot tell an apnea from other causes of a dip, and it would miss apneas that cause little or no drop. That is why my project is about measurement accuracy and oxygen dips, not about diagnosing sleep apnea.

## Slide 4
Design
The wearable.
3D design of a later version (v2): sealed case
Exploded: every v2 part at its real size
Prototype v1
armband + plug-in wires
Not built yet
parts list ready
MAX30102
red + infrared finger sensor
1 / second
SpO₂ + heart rate
Interactive 3D ›
Night Signal
4
Notes: [0:40] This is the design. The first prototype keeps things simple: an ESP32 board in a running armband, a MAX30102 sensor in a velcro finger cuff, and a USB cable for power, with every wire plugged in. It reads oxygen and heart rate once per second. The 3D model shows a possible later version in a sealed case. The prototype has not been built yet; the parts list and build guide are ready.

## Slide 5
How it works
From fingertip to data file.
01
Finger sensor
MAX30102 · red + infrared light
02
ESP32 on the arm
computes SpO₂ and pulse once per second
03
Bluetooth or USB
one line of data every second
04
App + analysis
signal quality, desaturation events, agreement
A device check runs before every session (tested so far on a simulated device).
$ python check_device.py --port /dev/pts/3 (simulated device)
[PASS] Data arriving 1 reading/s
[PASS] Self-test oxygen OK · motion OK
[PASS] Finger on sensor 100%
[PASS] Believable values SpO2 97–98%, HR 60–64
RESULT: READY
Firmware re-checks both sensors every 30 s.
No finger: readings are marked invalid and excluded.
A broken sensor gives “NOT READY” (checked with the simulated device).
Real hardware has not been tested yet.
Night Signal
5
Notes: [0:35] The finger sensor's light readings go to the ESP32, which calculates oxygen and pulse once per second and sends each reading over Bluetooth or USB to my app and analysis code. Every session will start with a device check that must say READY. So far I have tested this check only on a simulated device, where it also correctly reported a broken sensor; it still has to be tested on the real hardware.

## Slide 6
Experimental protocol · planned
How I will test it.
1
Approvals first Ms. Ireland, the ethics committee and signed consent, before any data
2
Accuracy sessions (main) seated; wearable on one finger, reference on the other; SpO₂ + heart rate every 2 min for 30 min; several sessions
3
Signal-quality checks finger on, sensor-valid flag, believable range, movement excluded
4
Overnight recordings (if approved) signal quality and desaturation events per valid hour; not verifiable overnight
5
Breath-hold test (optional, if approved) awake and supervised; are induced dips flagged? Not a test of sleep apnea
Safety
No testing on anyone, including me, before approval and consent
Breath-holds only if approved: awake, seated, supervised, 20 s at most, never asleep
Stop at any dizziness or discomfort
Not a medical device; no diagnosis
Night Signal
6
Notes: [0:50] This is my planned protocol. Nothing will be tested on anyone, including me, until my teacher accepts this revised proposal, the ethics committee approves, and consent is signed. The main test is accuracy: seated at rest, I wear my device on one finger and the reference oximeter on the other hand, and I record both oxygen and heart rate every two minutes for thirty minutes, over several sessions. Every reading must pass signal-quality checks. If approved, overnight recordings will measure signal quality and desaturation events, but those events cannot be verified because the reference oximeter does not record overnight. An optional breath-hold test, only if approved, would check whether short, awake dips are flagged; it does not test sleep apnea.

## Slide 7
The app
The companion app.
Night report (demo data)
Live + device health (demo)
Night tab: oxygen chart, flagged desaturation events, events per hour of valid recording, and % valid signal.
Live tab connects to the wearable (USB or Bluetooth) and runs the device checks every second.
Saving a session gives the same CSV the analysis uses, so every number can be traced.
Everything shown so far is labelled demonstration data. Heart and breathing tabs are exploratory ideas.
Open the app ›
Scan to try it. A demo device is built in.
Night Signal
7
Notes: [0:30] This is my companion app. The Night tab shows the oxygen chart, the desaturation events it flagged, the event rate per hour of valid recording and how much of the signal was valid. The Live tab connects to the wearable and runs the device checks. Everything you see so far is clearly labelled demonstration data.

## Slide 8
Results · not yet collected
What will be measured.
No real data yet
Measure | How it is calculated | Demonstration (simulated) | Real result
SpO₂ agreement | device − reference, paired every 2 min: bias, 95% limits | +0.07 (−1.47 to +1.61) points | pending
Heart-rate agreement | same pairing, in beats per minute | −0.0 (−2.3 to +2.3) bpm | pending
Valid signal | finger on, sensor-valid, 70–100%, no movement | 98% (6.88 of 7.0 h) | pending
Desaturation events | ≥ 3 points below a 120-s baseline for ≥ 10 s | 19 events | pending
Desaturation event rate | events ÷ hours of VALID recording | 2.8 per valid hour (19 ÷ 6.88 h) | pending
Breath-hold dips flagged (if approved) | flags within ±30 s of each logged hold | not simulated | pending
Demonstration values come from simulated data. They only show that the analysis works; they are not findings. The simulated “reference” was made from the same invented data. The event rate is not an apnea–hypopnea index.
Night Signal
8
Notes: [0:40] These are the results I will collect. I have not collected any real data yet. The table shows each measure, how it is calculated, and a demonstration value from simulated data, which only proves that my analysis code runs; they are not findings. The event rate is the number of desaturation events divided by the hours of valid signal, not hours in bed, and it is not an apnea-hypopnea index. The last column will be filled in with real results before January eleventh.

## Slide 9
Results · demonstration
How the results will be shown.
Simulated data
Red bands = flagged desaturation events (simulated night)
Bland–Altman agreement chart (simulated pairs)
Night Signal
9
Notes: [0:30] These two charts show how the results will be presented, using simulated data. On the left, the oxygen line with each flagged desaturation event as a red band. On the right, a Bland-Altman chart, the standard way to compare two measuring devices: each dot is a pair of readings, and the dashed lines show the range that ninety-five percent of differences fall in. With real data, that range is what tests my hypothesis.

## Slide 10
Method · signal quality
Only good readings count.
Finger on the sensor
Infrared level shows a finger is present; otherwise the reading is excluded.
Sensor confidence
The sensor marks each SpO₂ reading valid or invalid; invalid ones are excluded.
Believable range
SpO₂ outside 70–100% is excluded as an error.
Movement
5 s on each side of a sudden movement is excluded (motion distorts the light signal).
Desaturation event rate = flagged events ÷ hours of valid signal
Not hours in bed and not sleep time (the device cannot measure sleep). An event may never span a gap in the valid data. Each report states the % of valid signal.
Night Signal
10
Notes: [0:35] Only good readings count. A reading is used only if a finger is on the sensor, the sensor marks it valid, it is in a believable range, and there was no sudden movement within five seconds. The event rate is the number of flagged events divided by the hours of valid signal. It is not per hour of sleep, because my device cannot measure sleep, and every report states how much of the signal was valid.

## Slide 11
Main analysis · plan
How I will interpret the results.
Agreement
If 95% of SpO₂ differences fall within ±3 points of the reference at rest, the hypothesis is supported for these conditions. The reference itself is only ±2 points.
Desaturation events
A flagged event means an oxygen dip, not an apnea. Overnight events cannot be checked, because the reference cannot record overnight.
Breath-hold test (if approved)
Shows whether awake, induced dips are flagged at the logged times. It does not show that sleep apnea can be detected during sleep.
What would go against it
Limits wider than ±3 points, a consistent bias, a low % of valid signal, or logged dips that are missed.
Night Signal
11
Notes: [0:45] This is how I will interpret the results. If ninety-five percent of the oxygen differences fall within three points of the reference at rest, my hypothesis is supported for those conditions, keeping in mind that the reference is itself accurate to about two points. A flagged event means an oxygen dip, not an apnea, and overnight events cannot be checked because the reference does not record overnight. The breath-hold test, if approved, shows only whether awake dips are flagged. Wider limits, a consistent bias, too little valid signal, or missed dips would count against my hypothesis.

## Slide 12
Main analysis
Sources of error and limitations.
Measurement
Movement, finger pressure, cold hands and room light distort the light signal
Pulse oximeters can be less accurate on darker skin (Sjoding et al., 2020)
The reference oximeter is only accurate to about ±2 points
4-second averaging can smooth very short dips
Method
Oxygen and heart rate only: no airflow, breathing effort or sleep staging, so apnea cannot be identified
Awake rest is not the same as sleep; breath-holds are not apneas
One participant: results cannot be generalized
The reference cannot record overnight, so night events are unverified
Engineering estimate (to be measured). Bluetooth draws roughly 100 mA, so a 500 mAh battery would last only about 4–5 hours. That is why prototype v1 is planned to run on USB power.
Night Signal
12
Notes: [0:40] Sources of error in measurement: movement, finger pressure, cold hands and room light can distort the light signal; research has shown pulse oximeters can be less accurate on darker skin; and the reference is only accurate to about two points. In the method: my device measures only oxygen and heart rate, so it cannot identify apnea; sitting awake is not the same as sleep, and a breath-hold is not an apnea; there is only one participant; and overnight events cannot be verified. I also estimated that a small battery would last only four to five hours, which is why the first prototype is planned to use USB power; I still have to measure that.

## Slide 13
Project status
What is done, and what is planned.
Done
Design, parts list and build guide
Firmware written (not yet run on hardware)
Analysis software and simulator, tested on simulated data
App and 3D model
Scope revised with Ms. Ireland (Oct 9); revised proposal and ethics package drafted
Planned or pending
Ms. Ireland’s review of the revised proposal
Ethics approval and signed consent
Build and check the prototype
Accuracy sessions against the reference
Overnight recordings and optional breath-hold test (if approved)
Real results and analysis (by January 11)
Night Signal
13
Notes: [0:35] To be clear about where the project stands: the design, firmware, analysis software, app and 3D model are done, and the software has been tested only on simulated data. My teacher agreed to this revised scope on October ninth. Still pending are her review of the revised proposal, ethics approval and consent, building the prototype, and all of the real measurements.

## Slide 14
Conclusion
No conclusion yet.
No real data has been collected, so the hypothesis has not been tested. This slide will be written after the accuracy sessions.
What this project will be able to show
How closely the wearable agrees with a reference oximeter at rest
How much of a recording gives a valid signal
Whether flagged desaturation events match logged dips (if approved)
What it cannot show
Whether anyone has, or does not have, sleep apnea
App
3D model
Thank you. Questions?
Night Signal
14
Notes: [0:30] I do not have a conclusion yet, because no real data has been collected. After the accuracy sessions, this project will show how closely the wearable agrees with a reference oximeter at rest, how much of a recording gives a valid signal, and, if approved, whether flagged dips match logged ones. It cannot show whether anyone has sleep apnea. Thank you; I am happy to take questions.

## Slide 15
Appendix · not presented
Appendix A · Materials
Parts, exact sizes and where to buy.
Part | Size | Purpose | Buy
AITRIP ESP32 ESP-WROOM-32 (30-pin, CP2102, USB-C) | ≈ 52 × 28 mm · pins pre-soldered | Processor + Bluetooth Classic | Amazon.ca ›
HiLetgo MAX30102 sensor | 14 × 14 mm · 4 pins to solder | SpO₂ + heart rate (finger clip) | Amazon.ca ›
SHILLEHTEK GY-521 MPU-6050, pre-soldered (2-pack) | ≈ 21 × 16 mm | Movement check + position (exploratory) | Amazon.ca ›
ELEGOO 120 Dupont jumper wires (F-F, M-F, M-M) | 20 cm each | Plug-in wiring, no soldering | Amazon.ca ›
Running armband phone pouch | fits phones up to 6.9 in | Holds the ESP32 on the forearm | Amazon.ca ›
Anker Powerline+ USB-A to USB-C cable | 3 m (10 ft) | All-night power from a phone charger | Amazon.ca ›
Anker USB-C to USB-A adapter (2-pack) | USB-C → USB-A | Plug the cable into a MacBook | Amazon.ca ›
VELCRO Brand 1 in × 30 ft roll | 25 mm wide · cut ≈ 80 mm | Finger loop | Amazon.ca ›
Elite Medica fingertip pulse oximeter | confirm Health Canada licence | Reference for the accuracy test | Amazon.ca ›
Every part is on Amazon.ca (click Buy). Prices change and several items are multi-packs. Only the MAX30102’s 4 header pins need soldering (about 5 minutes); everything else plugs in.
Notes: [0:00] Appendix — not presented. Full parts list with exact dimensions and links.

## Slide 16
Appendix · not presented
Appendix B · Full protocol (planned)
Full experimental protocol (planned, not yet started).
1
Approvals first. Ms. Ireland accepts the revised proposal, the ethics committee approves, and informed consent is signed (participant and parent/guardian). No data is collected from anyone, including me, before all three.
2
Build and device check. MAX30102 → 3V3 / GND / GPIO 21 / 22; GY-521 → VIN / GND / SDA→GPIO 33 / SCL→GPIO 32 (two separate I²C buses); USB power. check_device.py must report READY before every session.
3
Accuracy sessions (main test). Seated, awake, at rest, warm hands. Wearable on one index finger, reference oximeter on the other hand. Every 2 min: time, reference SpO₂ and heart rate (15 pairs per 30-min session); several sessions on different days. validate.py: bias, 95% limits of agreement, mean absolute difference.
4
Signal-quality checks. Each 1-s reading counts only if a finger is present, the sensor marks it valid, SpO₂ is 70–100%, and there is no sudden movement within 5 s. Every report states the % of valid signal.
5
Overnight recordings (only if approved). % valid signal and desaturation events per hour of valid recording. The reference cannot record overnight, so these events cannot be verified. The rate is not an apnea–hypopnea index.
6
Breath-hold test (optional, only if approved). Awake, seated, adult-supervised, holds of at most 20 s, stop at any discomfort; start and end times logged. Tests only whether induced dips are flagged; it does not validate detecting sleep apnea during sleep.
7
Analysis. analyze.py (events, valid hours) and validate.py (agreement). Position, heart-rate and breathing-rate scripts are exploratory (Appendix D) and are not used to test the hypothesis.
8
Controls. Same participant, finger and cuff tightness, room and lighting, firmware, reference oximeter and detection settings (3-point drop, ≥ 10 s, 120-s baseline).
Notes: [0:00] Appendix — not presented. Planned step-by-step protocol, including approvals, signal-quality checks and controls. None of these steps has been carried out yet.

## Slide 17
Appendix · not presented
Appendix C · Design plans
Wiring (v1) and case layout (v2).
From | To (ESP32) | Notes
MAX30102 VIN / GND | 3V3 / GND | never 5 V
MAX30102 SDA / SCL | GPIO 21 / 22 | I²C bus 0
GY-521 VCC / GND | VIN / GND | 5 V from USB
GY-521 SDA / SCL | GPIO 33 / 32 | I²C bus 1, 100 kHz
Power | USB-C port | 3 m cable to charger
Status LED | GPIO 2 | blinks each reading
v2: the stack inside the 25 mm-tall case
Planned v2: a 70 × 45 × 29 mm box with its own battery. Layer heights: battery 6 mm + ESP32 with pins ≈ 13 mm + GY-521 ≈ 3 mm ≈ 22 mm, inside the box’s 25 mm. v1 uses each sensor’s own pins, so nothing needs splicing.
Notes: [0:00] Appendix — not presented. Prototype v1 wiring table, and the planned v2 case layout with layer heights. Neither has been built yet.

## Slide 18
Appendix · not presented
Appendix D · Exploratory ideas
Exploratory ideas (simulated data only).
Idea (script) | Demonstration output (simulated) | Why it is not a finding
Body position (position.py) | events per valid hour: back 3.8, stomach 3.2, left 1.3, right 1.1 | simulated; few hours per position; not an apnea measure
Machine-learning flagger (train_model.py) | recall 0.63 vs rule-based 0.63, on simulated labels | labels are invented; breath-hold labels would not validate apnea detection
Heart-rate patterns (heart.py) | 1 fast stretch (> 100 bpm), 1 very slow, 1 unsteady | per-second optical heart rate cannot identify arrhythmias
Breathing-rate estimate (signals.py, asthma.py) | 13.5 breaths/min; higher late in the simulated night | estimated from heart-rate rhythm, never measured; cannot detect asthma
Device check (check_device.py) | simulated device: healthy → READY; broken motion sensor → NOT READY | not yet run on real hardware
Demonstration data only. These ideas are outside the revised scope and are not used to test the hypothesis.
All code, data tools and raw CSV format on GitHub ›
Build guide: buy, build, connect ›
Notes: [0:00] Appendix — not presented. Exploratory analyses shown only on simulated demonstration data. None of these numbers is a finding, and none of these ideas is part of the revised research question.

## Slide 19
Appendix · not presented
Bibliography · APA
References.
American Academy of Sleep Medicine. (2014). International classification of sleep disorders (3rd ed.).
Benjafield, A. V., et al. (2019). Estimation of the global prevalence and burden of obstructive sleep apnoea: A literature-based analysis. The Lancet Respiratory Medicine, 7(8), 687–698.
Berry, R. B., et al. (2012). Rules for scoring respiratory events in sleep. Journal of Clinical Sleep Medicine, 8(5), 597–619.
Bland, J. M., & Altman, D. G. (1986). Statistical methods for assessing agreement between two methods of clinical measurement. The Lancet, 327(8476), 307–310.
International Organization for Standardization. (2017). Medical electrical equipment — Part 2-61: Particular requirements for basic safety and essential performance of pulse oximeter equipment (ISO 80601-2-61:2017).
Jubran, A. (2015). Pulse oximetry. Critical Care, 19, 272.
Kapur, V. K., et al. (2017). Clinical practice guideline for diagnostic testing for adult obstructive sleep apnea. Journal of Clinical Sleep Medicine, 13(3), 479–504.
Maxim Integrated. (2020). MAX30102 high-sensitivity pulse oximeter and heart-rate sensor [Datasheet].
Sjoding, M. W., Dickson, R. P., Iwashyna, T. J., Gay, S. E., & Valley, T. S. (2020). Racial bias in pulse oximetry measurement. New England Journal of Medicine, 383(25), 2477–2478.
Task Force of the European Society of Cardiology and NASPE. (1996). Heart rate variability: Standards of measurement, physiological interpretation, and clinical use. Circulation, 93(5), 1043–1065.
Notes: [0:00] Appendix — not presented. References in APA style.